## Slide 1: CS 5187: Vision and Image Lecture 1-3 Edge Detection
Dr. Dapeng Oliver Wu
City University of Hong Kong
Department of Computer Science
Semester A, 2026/27

## Slide 2: Edge detection
TexPoint fonts used in EMF.
Read the TexPoint manual before you delete this box.: AAA
Convert a 2D image into a set of curves
  Extracts salient features of the scene
  Contain higher level semantic info, than pixels

## Slide 3: Edge detection
Goal: Identify visual changes (discontinuities) in an image.
Intuitively, semantic information is encoded in edges.
What are some ‘causes’ of visual edges?
Source: D. Lowe

## Slide 4: Origin of Edges
Edges are caused by a variety of factors
depth discontinuity
surface color discontinuity
illumination discontinuity
surface normal discontinuity

## Slide 5: Images as functions…
Edges look like steep cliffs

## Slide 6: Closeup of edges
Source: D. Hoiem

## Slide 7: Closeup of edges
Source: D. Hoiem

## Slide 8: Closeup of edges
Source: D. Hoiem

## Slide 9: Closeup of edges
Source: D. Hoiem

## Slide 10: Characterizing edges
An edge is a place of big change in the image intensity function
image
intensity function (along horizontal scanline)
first derivative
edges correspond to extrema of derivative
Source: L. Lazebnik

## Slide 11: Image derivatives
How can we differentiate a digital image F[x,y]?
  Option 1: reconstruct a continuous image, f, then compute the derivative
  Option 2: take discrete derivative (finite difference)
1 | -1 | 
How would you implement this by a linear filter?
 | -1 | 
 | 1 | 
:
:
Source: S. Seitz

## Slide 12: Image gradient
The gradient points toward the direction of the biggest increase in intensity
The gradient of an image:
The edge strength is given by the gradient magnitude:
The gradient direction is given by:
Source: Steve Seitz

## Slide 13: Image gradient
Source: L. Lazebnik

## Slide 14: Effects of noise
Where is the edge?
Source: S. Seitz
Noisy input image
Notes: How to fix?

## Slide 15: Solution: smooth first
f
h
f * h
Source: S. Seitz
To find edges, look for peaks in

## Slide 16: Associative property of convolution
Differentiation can be implemented by convolution, and convolution is associative:
This saves us one operation:
f
Source: S. Seitz

## Slide 17: The 1D Gaussian and its derivatives

## Slide 18: Derivative of Gaussian filter
x-direction
y-direction

## Slide 19: The Sobel operator
Common approximation of derivative of Gaussian
-1 | 0 | 1
-2 | 0 | 2
-1 | 0 | 1
1 | 2 | 1
0 | 0 | 0
-1 | -2 | -1
  The standard defn. of the Sobel operator omits the 1/8 term
    doesn’t make a difference for edge detection
    the 1/8 term is needed to get the right gradient magnitude

## Slide 20: Sobel operator: example
Source: Wikipedia
x-gradient
y-gradient
gradient magnitude

## Slide 21
Sobel operator
Original
Orientation
Magnitude

## Slide 22: Laplacian of Gaussian (LoG)
Consider
Laplacian of Gaussian
operator
Where is the edge?
Zero-crossings of bottom graph

## Slide 23: 2D edge detection filters
is the Laplacian operator:
Laplacian of Gaussian
Gaussian
derivative of Gaussian
Notes: Blurring an image with a Gaussian and then taking its Laplacian is equivalent to convolving directly with the Laplacian of Gaussian (LoG) filter

## Slide 24: Laplacian for Edge Detection

## Slide 25: Using the LoG Function
The LoG function will be
  Zero far away from the edge
  Positive on one side
  Negative on the other side
  Zero just at the edge
Therefore, it can be used as an edge operator
BUT, is this good enough?

## Slide 26: Designing an edge detector
Criteria for a good edge detector:
  Good detection: the optimal detector should find all real edges, ignoring noise or other artifacts
  Good localization
    the edges detected must be as close as possible to the true edges
    the detector must return one point only for each true edge point
Cues of edge detection
  Differences in color, intensity, or texture across the boundary
  Continuity and closure
  High-level knowledge
Source: L. Fei-Fei

## Slide 27: Canny edge detector
This is probably the most widely used edge detector in computer vision
J. Canny, A Computational Approach To Edge Detection, IEEE Trans. Pattern Analysis and Machine Intelligence, 8:679-714, 1986.
Source: L. Fei-Fei

## Slide 28: Example
original image (Lena)

## Slide 29: Finding edges
gradient magnitude

## Slide 30
thresholding
Finding edges
where is the edge?

## Slide 31: Get Orientation at Each Pixel
theta = atan2(gy, gx)

## Slide 32: Non-maximum suppression
Check if pixel is local maximum along gradient direction
Picture from Prem K Kalra
Perform comparisons on the edge strength of the current pixel with the edge strength of the pixel in the positive and negative gradient directions.
Preserve the largest and suppress the others.

## Slide 33: Before Non-max Suppression

## Slide 34: After Non-max Suppression

## Slide 35
thresholding
Finding edges

## Slide 36
thinning
(non-maximum suppression)
Finding edges

## Slide 37: Canny edge detector
Filter image with derivative of Gaussian
Find magnitude and orientation of gradient
Non-maximum suppression
Linking and thresholding (hysteresis):
  Define two thresholds: low and high
  Use the high threshold to start edge curves and the low threshold to continue them
Source: D. Lowe, L. Fei-Fei
MATLAB: edge(image,‘canny’)

## Slide 38: ‘Hysteresis’ thresholding
Two thresholds – high and low
Grad. mag. > high threshold? = strong edge
Grad. mag. < low threshold? noise
In between = weak edge
‘Follow’ edges starting from strong edge pixels
Continue them into weak edges
    Connected components (Szeliski 3.3.4)
Source: S. Seitz

## Slide 39: Final Canny Edges

## Slide 40: Effect of  (Gaussian kernel spread/size)
Original
The choice of  depends on desired behavior
  large  detects large scale edges
  small  detects fine features
Source: S. Seitz

## Slide 41: Canny Characteristics
The Canny operator gives single-pixel-wide images with good continuation between adjacent pixels
It is probably the most widely used edge operator today; no one has done better since it came out in the late 80s. Many implementations are available.
It is very sensitive to its parameters, which need to be adjusted for different application domains.
J. Canny, A Computational Approach To Edge Detection, IEEE Trans. Pattern Analysis and Machine Intelligence, 8:679-714, 1986.